## Slide 1: Using ADC in atmega32
CSE 315
Md. Iftekharul Islam Sakib

## Slide 2: Learning objective
Why do we need ADC?
What is ADC?
ADC in ATmega32
A simple example

## Slide 3: Recap
MCU is a digital processor
  Works with binary data
    Just 2 voltage levels
MCU needs to collect information from the real world
  Temperature, Pressure, Humidity, Sound …
    Continuous property
    Infinite possible values
Why do we collect information?
  To analyze the situation
  To take appropriate actions

## Slide 4: ReCAP
But how to collect information?
  Sensors: Convert physical property into analog signal
    Voltage, Current, Resistance, …
How can MCU recognize these signal?
  Need to convert into digital data
  How?
    Approximation
  Need something special!

## Slide 5: Typical embedded application

## Slide 6: ADC: Quick review

## Slide 7: A-to-D conversion
Two related steps
Sampling (Approximating the X-axis)
  the analogue signal is extracted at regularly spaced time instants
  the samples have real values
Quantization (Approximating the Y-axis)
  the samples are quantized to discrete levels
  each sample is represented as a binary value

## Slide 8: Sampling an analogue signal

## Slide 9: Quantizing the sampled signal

## Slide 10: Quantizing the sampled signal

## Slide 11: Quantizing the sampled signal

## Slide 12: 8-bit adc

## Slide 13: example

## Slide 14: A question
What is the difference between an ADC and a digital input pin?

## Slide 15: The ADC in ATmega32
The ADC has a 10-bit resolution.
  The binary output has n = 10 bits
The ADC has 8 input channels
  Analogue input can come from 8 different sources
  However, it performs conversion on only one channel at a time
If default reference voltage Vref = 5V is used
  step size: 5 V/1024 = 4.88mV
The clock rate of the ADC can be different from the CPU clock rate
  One ADC conversion takes 13 ADC cycles
  An ADC prescaler will decide the ADC clock rate

## Slide 16: Relevant pins

## Slide 17: Block diagram

## Slide 18: Main aspects
What are the relevant ADC registers?
  ADCMUX
  ADCH/ADCL
  ADCCSRA
  SFIOR
What are the steps to use the ADC?
How to use ADC interrupt?

## Slide 19: ADC Multiplexer Selection Register (ADCMUX)

## Slide 20: Selecting reference voltage Vref

## Slide 21: ADC Recommended connection

## Slide 22: Selecting input source

## Slide 23: Selecting input source

## Slide 24: ADCH & ADCL registers
Important
  When retrieving digital output, register ADCL must be read first, before register ADCH.

## Slide 25: ADC Control and Status Register (ADCCSRA)

## Slide 26: ADC clock

## Slide 27: Special Function IO Register (SFIOR)

## Slide 28: Steps to use the ADC

## Slide 29: Simple Example

## Slide 30: Simple Example

## Slide 32: Simple Example: Using ADC interrupt

## Slide 34: Temperature sensor

## Slide 35: Temperature sensor

## Slide 36: Interfacing LM34 to AVR

## Slide 37: Interfacing LM34 to AVR
If we use the internal 2.56 V reference voltage
  step size would be 2.56 V/1024 = 2.5 mV
  This makes the binary output of the ADC four times the real temperature
  Divide the binary output by 4 to get the real temperature

## Slide 38: Interfacing LM34 to AVR

## Slide 39: Interfacing LM34 to AVR
#include <avr/io.h> //standard AVR header
int main (void)
{
  DDRB = 0xFF; //make Port B an output
  ADCSRA = 0x87; //make ADC enable and select ck/128
  ADMUX = 0xE0; //2.56 V Vref and ADCO single-ended
  //data will be left-justified
  while (1 ){
    ADCSRA |= (l<<ADSC); //start conversion
    while((ADCSRA & (l<<ADIF))==0); //wait for end of conversion
    PORTB = ADCH; //give the high byte to PORTB
  }
  return 0;
}

## Slide 40: Auto trigger logic

## Slide 41: Auto Trigger Source

## Slide 42: Timer: Normal vs. CTC mode

## Slide 43: A practical problem
We need to sample an analog signal @ 20 kHz sampling frequency
The only way to do this correctly
  use auto-triggering with exact time intervals
Let’s see how can we do this using Timer0

## Slide 44: Solution Overview
Assume
  system clock frequency = 16 MHz
  Timer0 prescaler = 8
To ensure 20 kHz sampling frequency
  Time between successive ADC conversions?
    50us
  Use Timer0 to trigger ADC every 50us
  How to trigger Timer0 compare match every 50us?
    Need to count?
      50us/(8/16000000) = 100
      From 0 to 99
      Set OCR0 = 99

## Slide 45: Solution Overview
  Timer0 compare match trigger every 50us
    Need to count?
    50us/(8/16000000) = 100
    From 0 to 99
    Set OCR0 = 99
    Why 99 instead of 100 ?

## Slide 46: Solution Overview
Now let’s select ADC prescaler properly
  ADC conversion must be completed before next Timer0 compare match occur
One auto triggered ADC conversion time takes 13.5 ADC cycles

## Slide 47: Solution Overview
Now let’s select ADC prescaler properly
  ADC conversion must be completed before next Timer0 compare match occur
One auto triggered ADC conversion time takes 13.5 ADC cycles

## Slide 48: Solution Overview
To fit in to 50us window we can select prescaller up to 32
Gives enough time to
  Complete auto triggered ADC cycle
  Clear Timer0 compare match flag
  Store ADC value within one sample period
  …

## Slide 49: Solution Overview
ADC prescaller = 32
Gives enough time to
  Complete auto triggered ADC cycle
  Clear Timer0 compare match flag
  Store ADC value within one sample period
  …

## Slide 50: Complete code for Atmega328
http://www.embedds.com/adc-on-atmega328-part-2/