## Slide 1: Microprocessors and Microcontrollers
Md. Tareq Mahmood
Original slides made by Azad Abdus Salam
SERIAL COMMUNICATION USING ATMEGA16/32

## Slide 2: Types of Data Communication
Data Communication
Serial
Parallel
Synchronous
Asynchronous

## Slide 3: Serial vs. Parallel Communication
Computers transfer data in two ways: parallel and serial.
Parallel: Several data bits are transferred simultaneously, e.g. printers and hard disks.
Serial: A single data bit is transferred at one time, e.g. bluetooth and USB.

## Slide 4: Why Serial Communication ???
longer distances (fewer wires/cables)
easier to synchronize
fewer IO pins
lower cost

## Slide 5: Synchronous Communication
The clocks of the sender and receiver are synchronized.
A block of characters, enclosed by synchronizing bytes, is sent at a time.
Faster transfer and less overhead
Example:
  Serial Peripheral Interface (SPI) by Motorola

## Slide 6: Asynchronous Communication
The clocks of the sender and receiver are not synchronized.
One character (8 or 7 bits) is sent at a time, enclosed between a start bit and one or two stop bits. A parity bit may be included.
Examples:
  RS232 (part of) by Electronic Industry Alliance.
  USART of ATmega16

## Slide 7: Transmission Modes/ Channel Types
Transmission Modes
Simplex
Half-duplex
Full-duplex

## Slide 8: Transmission Modes/ Channel Types
Simplex
Half-duplex
Full-duplex

## Slide 9: Serial communications in ATmega16
ATmega16 provides three subsystems for serial communications
  Universal Synchronous & Asynchronous Serial Receiver & Transmitter (USART)
  Serial Peripheral Interface (SPI)
  Two-wire Serial Interface (TWI)

## Slide 10: USART
Supports full-duplex mode between a receiver and transmitter
Typically used in asynchronous communication.
  We focus more on the asynchronous communication!! Often called UART
  An asynchronous UART can operate using 2 wires: Transmit (Tx) and Receive (Rx)
Typical speed: 960bps up to 57.6kbps

## Slide 11: USART

## Slide 12: Serial Peripheral Interface (SPI)
The receiver and transmitter share a common clock line.
The device considered the 'Master' provides a clock signal used to synchronize data transactions between the two devices.
Supports higher data rates.
A SPI interface uses a 3-wire system
  MOSI, MISO, SCK

## Slide 13: Serial Peripheral Interface (SPI)

## Slide 14: Two-wire Serial Interface (TWI)
Network several devices such as microcontrollers and display boards, using a two-wire bus.
7 bit address
Up to 128 devices are supported
Each device has a unique address and can exchange data with other devices in a small network.
TWI is ATmega32 version of Phillips’ I2C
  Inter-Integrated Circuit, pronounced "I squared C"

## Slide 15: Two-wire Serial Interface (TWI)
A sample TWI network connecting 3 devices with TWI master.

## Slide 16: Two-wire Serial Interface (TWI)

## Slide 17: Serial communications terminology
Parity bit: a single bit that is sent together with data bits to make the total number of 1’s even (for even parity) or odd (for odd parity)
  used for error checking.
Start bit: to indicate the start of a character. Its typical value is 0.
Stop bit: to indicate the end of a character. Its typical value is 1

## Slide 18: Data Framing - Asynchronous
A frame starts with the start bit followed by the least significant data bit.

## Slide 19: Data Framing - Asynchronous
Example:

## Slide 20: USART in ATmega16 – An Overview
baud rates from 960bps up to 57.6kbps
  technically baud rate refers to symbols per second
  for our case baud rate is equal to bit-rate
character size: 5 to 9 bits
1 start bit
1 or 2 stop bits
parity bit (optional: even or odd parity)

## Slide 21: USART – Hardware Elements
USART Transmitter:
  to send a character through TxD pin.
  to handle start/stop bit framing, parity bit, shift register.
USART Receiver:
  to receive a character through RxD pin.
  to perform the reverse operation of the transmitter

## Slide 22: PINOUT
RXD
  To recieve
TXD
  To transmit

## Slide 23: USART - Registers
Three set of registers
USART Baud Rate Registers
  UBRRH and UBRRL
  Sets the speed of communication
USART Control and Status Registers
  UCSRA, UCSRB, and UCSRC
USART Data Register
  UDR
  Used to read and write actual data!

## Slide 24: Baud rate
The number of bits sent per second (bps).
Strictly speaking, baud rate is the number of symbols per second.
Or, how many times signal changes states
As we have only two symbols 0 and 1, here baud rate is equal to bps

## Slide 25: Setting Baud Rate
Two register UBRRH and UBRRL are used together to set the baud rate
There is also a double speed transmission mode, where the 16 is replaced by 8 in the formula
Must be 0 when setting the baud rate

## Slide 26: Setting Baud Rate – An Example
UBRR = 1000000/(16 × 1200) ─ 1 = 51d = 0033H.
Therefore, UBRRH = 0x00 and UBRRL = 0x33
Find UBRR registers for baud rate of 1200bps, assuming system clock is 1MHz

## Slide 27: USART Control and Status Register A (UCSRA)
Used for checking status of communication

## Slide 28: USART Control and Status Register B (UCSRB)

## Slide 29: USART Control and Status Register C (UCSRC)

## Slide 30: Setting character size
Characters can be 5 to 9 bits long
Three bits are designated to configure the character size
  bit UCSZ2 (in register UCSRB)
  bit UCSZ1 and UCSZ0 (in register UCSRC)

## Slide 31: Setting character size

## Slide 32: USART Data Register - UDR
Register UDR is the buffer for characters sent or received through the serial port

## Slide 33: Learning Goals
Initializing the serial port.
Sending and receiving a character.
Sending/receiving formatted strings

## Slide 34: Initializing Serial Port

## Slide 35: Initialize ATmega16 for UART with the following parameters: baud rate 1200 bps, no parity, 1 stop bit, 8 data bits. Assume a clock speed of 1MHz and polling approach.

## Slide 36: C Code
void UART_init(void){ // Normal speed, disable multi-proc UCSRA = 0b00000000; // Enable Tx and Rx, disable interrupts UCSRB = 0b00011000; // Asynchronous mode, no parity, 1 stop bit, 8 data bits UCSRC = 0b10000110; // Baud rate 1200bps, assuming 1MHz clock UBRRL = 0x33; UBRRH = 0x00; }

## Slide 37: C Code
void UART_init(void){ // Normal speed, disable multi-proc UCSRA = 0b00000000; // Enable Tx and Rx, disable interrupts UCSRB = 0b00011000; // Asynchronous mode, no parity, 1 stop bit, 8 data bits UCSRC = 0b10000110; // Baud rate 1200bps, assuming 1MHz clock UBRRL = 0x33; UBRRH = 0x00; }

## Slide 38: C Code
void UART_init(void){ // Normal speed, disable multi-proc UCSRA = 0b00000000; // Enable Tx and Rx, disable interrupts UCSRB = 0b00011000; // Asynchronous mode, no parity, 1 stop bit, 8 data bits UCSRC = 0b10000110; // Baud rate 1200bps, assuming 1MHz clock UBRRL = 0x33; UBRRH = 0x00; }

## Slide 39: C Code
void UART_init(void){ // Normal speed, disable multi-proc UCSRA = 0b00000000; // Enable Tx and Rx, disable interrupts UCSRB = 0b00011000; // Asynchronous mode, no parity, 1 stop bit, 8 data bits UCSRC = 0b10000110; // Baud rate 1200bps, assuming 1MHz clock UBRRL = 0x33; UBRRH = 0x00; }

## Slide 40: C Code
void UART_init(void){ // Normal speed, disable multi-proc UCSRA = 0b00000000; // Enable Tx and Rx, disable interrupts UCSRB = 0b00011000; // Asynchronous mode, no parity, 1 stop bit, 8 data bits UCSRC = 0b10000110; // Baud rate 1200bps, assuming 1MHz clock UBRRL = 0x33; UBRRH = 0x00; }

## Slide 41: Sending a character (Polling)

## Slide 42: Write a C function to send a character through the serial port of ATmega16 (Polling)

## Slide 43: C Code
void UART_send(unsigned char data){ // wait until UDRE flag is set to logic 1 while ((UCSRA & (1<<UDRE)) == 0x00); UDR = data; // Write character to UDR for transmission }

## Slide 44: Receiving a character (Polling)

## Slide 45: Write a C function to receive a character through the serial port of ATmega16 (Polling)

## Slide 46: C Code
unsigned char UART_receive(void){ // Wait until RXC flag is set to logic 1 while ((UCSRA & (1<<RXC)) == 0x00); return UDR; // Read the received character from UDR }

## Slide 47: Sending/receiving formatted strings
Write two functions to send and receive a character through serial port.
  Already done - UART_send and UART_receive
2) In main program, call fdevopen() to designate the two functions as the handlers for standard output and standard input device.
3) Use printf/scanf as usual. Formatted strings will be sent/received through serial port.

## Slide 48: C Code
#include <avr/io.h> #include <stdio.h>
int main(void)
{ unsigned char a; // … Code to initialise baudrate, TXD, RXD, and so on is not shown here // Initialise the standard IO handlers stdout = fdevopen(UART_send, NULL); stdin = fdevopen(NULL, UART_receive); // Start using printf, scanf as usual while (1){ printf(“\n\rEnter a = "); scanf(“%d”, &a); printf(“%d”, a); } }

## Slide 49: Now, it is time to implement our knowledge in a sample application

## Slide 50: Program a camera to rotate repetitively
Connection Parameters
  8 data bit
  1 stop bit
  no parity bit
  baud rate 9600bps
Control: Sending character “4” or “6” turns the camera left or right, respectively

## Slide 51: Setting Baud Rate
In normal mode, the calculation leads to a UBR of 6.51-1 = 5.51
Hence the UBR would have to be set to 5 or, 6
Thus we will use double speed mode to be more precise

## Slide 52: C Code - Initialize
void USART_init(void)
{
UCSRA = 0b00000010; // double speed
UCSRB = 0b00011000; // Enable Tx and Rx, polling
UCSRC = 0b10000110; // Async mode, no parity, 1 stop bit, 8 data bits
//in double-speed mode, UBRR = clock/(8xbaud rate) - 1
UBRRH = 0;
UBRRL = 12; // Baud rate 9600bps, assuming 1MHz clock
}

## Slide 53: C Code – Main Loop
int main(void)
{
unsigned char i;
USART_init(); // initialise USART
while (1) {
for (i=0; i<10; i++)// rotate left 10 times
{
UART_send('4');
delay();
}
for (i=0; i < 10; i++)//rotate right 10 times {
UART_send('6');
delay();
}
}
}

## Slide 54: Sending 9 bit characters
The ninth bit must be written to the TXB8 bit in UCSRB before the low byte of the character is written to UDR

## Slide 55: Reception of 9 bit characters and status flags
Reading UDR changes the RXB8, FE, DOR and PE bits
Always read status from UCSRA and the 9th bit from RXB8 in UCSRB BEFORE
  reading data from UDR.

## Slide 56: Reception of 9 bit characters and status flags

## Slide 57: Transmission
To start transmission data is written in the buffer (UDR)
The buffered data will be moved to the Shift Register when the Shift Register is ready to send a new frame, i.e, it has no bits left to send.
    if it is in idle state (no ongoing transmission) or
    immediately after the last stop bit of the previous frame is transmitted.

## Slide 58: Reception
The receiver starts data reception when it detects a valid start bit.
Each bit that follows the start bit will be sampled at the baud rate or XCK clock, and shifted into the receive Shift Register until the first stop bit of a frame is received.
A second stop bit will be ignored by the receiver.

## Slide 59: Reception
When the first stop bit is received, a complete serial frame is present in the receive Shift Register, the contents of the Shift Register is then moved into the receive buffer.
The receive buffer can then be read from UDR.

## Slide 60: Checking Transmission Status
The USART transmitter has two flags that indicate its state:
  USART Data Register Empty (UDRE)
  Transmit Complete (TXC).
The Data Register Empty (UDRE) Flag indicates whether the transmit buffer is ready to receive new data.
  This bit is set when the transmit buffer is empty
  and not set when not empty ( has unmoved data to shift register).

## Slide 61: Checking Transmission Status
The Transmit Complete (TXC) Flag bit is set one when
  the entire frame in the transmit Shift Register has been shifted out, and
  there are no new data currently present in the transmit buffer.
The TXC Flag bit is automatically cleared when
  a transmit complete interrupt is executed, or
  it can be cleared by writing a one to its bit location

## Slide 62: Checking TXC flag to check transmission status
The TXC Flag must be cleared before each transmission (before UDR is written)
If, not, then what will be the problem ???

## Slide 63: Transmission using UDRIE Interrupt
The USART Data Register Empty Interrupt will be executed as long as UDRE is set.
  UDRE is cleared by writing UDR.
When interrupt-driven data transmission is used, the Data Register Empty Interrupt routine must
  either write new data to UDR in order to clear UDRE or
  disable the Data Register empty Interrupt
No such problem with TXCIE interrupt

## Slide 64: Reception using RXCIE interrupt
When the Receive Complete Interrupt Enable (RXCIE) in UCSRB is set, the USART Receive Complete Interrupt will be executed as long as the RXC Flag is set
The receive complete routine must read the received data from UDR in order to clear the RXC Flag
  otherwise a new interrupt will occur once the interrupt routine terminates.

## Slide 65: Double Speed Mode Disadvantage
The receiver will use half the number of samples (reduced from 16 to 8) for data sampling and clock recovery (syncing the internal clock to the incoming serial frames)
Hence, a more accurate baud rate setting and system clock are required.
For the transmitter, there are no downsides.

## Slide 66: Frame Error
A UART will detect a framing error when it does not see a "stop" bit at the expected "stop" bit time.
A FE (Frame Error) will be detected in the cases where the first stop bit is zero.
  The receiver ignores the second stop bit

## Slide 67: Data OverRun Error (DOR)
The Data OverRun (DOR) Flag indicates data loss due to a receiver buffer full condition.
A Data OverRun occurs when the receive buffer (UDR) is full (two characters), it is a new character waiting in the receive Shift Register, and a new start bit is detected.
If the DOR Flag is set there was one or more serial frame lost between the frame last read from UDR, and the next frame read from UDR.

## Slide 68: Disabling Transmission and Reception
The disabling of the transmitter (setting the TXEN to zero) will not become effective until ongoing and pending transmissions are completed
The disabling of reception is immediate
  Disabling reception flushes the receive buffer immediately

## Slide 69: Asynchronous Clock Recovery
The clock recovery logic synchronizes internal clock to the incoming serial frames.
The sample rate is 16 times the baud rate for Normal mode, and 8 times the baud rate for Double Speed mode.

## Slide 70: Asynchronous Clock Recovery
Samples denoted zero are samples done when the RxD line is idle (that is, no communication activity).
When the clock recovery logic detects a high (idle) to low (start) transition on the RxD line, the start bit detection sequence is initiated.

## Slide 71: Asynchronous Clock Recovery
The clock recovery logic uses samples 8, 9, and 10 for Normal mode, and samples 4, 5, and 6 for Double Speed mode
If two or more of these three samples have logical high levels (the majority wins), the start bit is rejected as a noise spike and the receiver starts looking for the next high to low-transition.

## Slide 72: Asynchronous Clock Recovery
If however, a valid start bit is detected, the clock recovery logic is synchronized and the data recovery can begin.
The synchronization process is repeated for each start bit.

## Slide 73: Asynchronous Data Recovery
The decision of the logic level of the received bit is taken by doing a majority voting of the logic value to the three samples in the center of the received bit.
The parity bit and the first stop bit is also sampled this way

## Slide 74: Resources
Comparison between UART, SPI, and I2C
  https://electronics.stackexchange.com/questions/37814/usart-uart-rs232-usb-spi-i2c-ttl-etc-what-are-all-of-these-and-how-do-th
  http://www.rfwireless-world.com/Terminology/UART-vs-SPI-vs-I2C.html

## Slide 75
☺

## Slide 76: SPI

## Slide 77: Serial Peripheral Interface (SPI)
The receiver and transmitter share a common clock line.
The device considered the 'Master' provides a clock signal used to synchronize data transactions between the two devices.
Supports higher data rates than UART.
A SPI interface uses a 3-wire system
  MOSI, MISO, SCK
  There is also a slave select pin, which is used to activate slave

## Slide 78: PIN Description
SPI uses 4 pins for communications
MISO – MISO stands for Master In Slave Out. MISO is the input pin for Master, and output pin for Slave device. Data transfer from Slave to Master takes place through this channel.
MOSI – MOSI stands for Master Out Slave In. This pin is the output pin for Master and input pin for Slave. Data transfer from Master to Slave takes place through this channel.

## Slide 79: PIN Description
3. SCK – This is the SPI clock line
Master generates a clock signal in this PIN which is fed to the slave
4. SS – This stands for Slave Select.
This pin is used to activate/select a slave

## Slide 80: SPI Connection: Single Slave

## Slide 81: SPI
Both, Master and Slave place the data (byte) they wish to transfer in their respective shift registers before the communication starts.
Master generates 8 clock pulses. After each clock pulse, one bit of information is transfer from Master to Slave and vice-versa.
After 8 clock pulses, Master would have received Slave’s data, whereas Slave would have Master’s data. And that’s why this is a full-duplex communication.

## Slide 82: SPI Master-slave Interconnection
Slave select line should activate slave before starting transmission and deactivate it after finishing communication.
Any free pin of the Master can be used to drive the Slave Select line of the slave
The SS line of Master, if configured as output is typically used to drive a slave

## Slide 83: Slave Select Line Functionality - Slave Mode
When the SPI is configured as a Slave, the Slave Select (SS) pin is always input.
When SS is held low, the SPI is activated
When SS is driven high, it will not receive incoming data.

## Slide 84: Slave Select Line Functionality - Master Mode
When the SPI is configured as a Master (MSTR in SPCR is set), the user can determine the direction of the SS pin.
If SS is configured as an output, the pin is a general output pin which does not affect the SPI system.
Typically, the pin will be driving the SS pin of the SPI Slave.

## Slide 85: Slave Select Line Functionality - Master Mode
When configured as a Master, the SPI interface has no automatic control of the SS line.
This must be handled by user software before communication can start.

## Slide 86: SPI Pin Overrides
When the SPI is enabled, the data direction of the MOSI, MISO, SCK, and SS pins is overridden according to following table

## Slide 87: Register Descriptions
Three registers deal with SPI:
SPCR – SPI Control Register
  It contains the bits to initialize SPI and control it.
SPSR – SPI Status Register
  This register is used to read the status of the bus lines.
SPDR – SPI Data Register
  The SPI Data Register is the read/write register where the actual data transfer takes place.

## Slide 88: SPI - Transmission Steps
The SPI Master initiates the communication cycle by pulling low the Slave Select pin of the desired Slave.
Master writes the byte to send in SPDR
Step 2 triggers the the SPI clock generator of the Master to generate the required clock pulses on the SCK line to interchange data.

## Slide 89: SPI - Transmission Steps
4. After shifting one byte, the SPI clock generator stops, setting the end of Transmission Flag (SPIF). If the SPI Interrupt is enabled an interrupt is issued.
5. The Master may continue to shift the next byte by writing it into SPDR, or signal the end of packet by pulling high the Slave Select line.

## Slide 90: SPI Control Register - SPCR
Bit 7 – SPIE: SPI Interrupt Enable
  This bit causes the SPI interrupt to be executed if SPIF bit in the SPSR Register is set
Bit 6 – SPE: SPI Enable
  written one to enable the SPI
Bit 5 – DORD: Data Order
  When the DORD bit is written to one, the LSB of the data word is transmitted first.
  When the DORD bit is written to zero, the MSB of the data word is transmitted first.

## Slide 91: SPI Control Register - SPCR
Bit 4 – MSTR: Master/Slave Select
  1 for Master and 0 for Slave
Bit 3 – CPOL: Clock Polarity
  The CPOL functionality is summarized below:

## Slide 92: SPI Control Register - SPCR
Bit 2 – CPHA: Clock Phase
  The settings of the Clock Phase bit (CPHA) determine if data is sampled on the leading (first) or trailing (last) edge of SCK.

## Slide 93: SPI Control Register - SPCR

## Slide 94: SPI Status Register - SPSR
Bit 7 – SPIF: SPI Interrupt Flag
  When a serial transfer is complete, the SPIF Flag is set. Interrupt is generated if enabled
  SPIF is cleared by hardware when executing the corresponding interrupt handling vector.
  Alternatively, the SPIF bit is cleared by first reading the SPI Status Register with SPIF set, then accessing the SPI Data Register (SPDR).

## Slide 95: SPI Status Register - SPSR
Bit 6 – WCOL: Write Collision Flag
  The WCOL bit is set if the SPI Data Register (SPDR) is written during a data transfer.
Bit 0 – SPI2X: Double SPI Speed Bit
  When this bit is written logic one the SPI speed (SCK Frequency) will be doubled when the SPI is in Master mode

## Slide 96: SPI Data Register - SPDR
The SPI Data Register is used for data transfer.
Writing to the register initiates data transmission.
Reading the register causes the Shift Register Receive buffer to be read.

## Slide 97: PINOUT

## Slide 98: SPI Pin Overrides
When the SPI is enabled, the data direction of the MOSI, MISO, SCK, and SS pins is overridden according to following table

## Slide 99: SPI – Sample Setup

## Slide 100: SPI – Sample Setup

## Slide 101: SPI – Master Config
void SPI_MasterInit(void)
{
/* Set MOSI and SCK output, all others input */
DDRB = (1<<DDB5)|(1<<DDB7);
/* Enable SPI, Master, set clock rate fck/16 */
SPCR = (1<<SPE)|(1<<MSTR)|(1<<SPR0);
}

## Slide 102: SPI – Slave Config
void SPI_SlaveInit(void)
{
/* Set MISO output, all others input */
DDRB = (1<<DDB6);
/* Enable SPI */
SPCR = (1<<SPE);
}

## Slide 103: SPI - Data sending
void SPI_MasterTransmit(char cData)
{
/* Start transmission */
SPDR = cData;
/* Wait for transmission complete */
while(!(SPSR & (1<<SPIF)));
}

## Slide 104: SPI - Data Receiving
char SPI_SlaveReceive(void)
{
/* Wait for reception complete */
while(!(SPSR & (1<<SPIF)));
/* Return data register */
return SPDR;
}

## Slide 105: How to perform duplex operation: send and receive simultaneously ?

## Slide 106: SPI – Data Exchange
char SPI_Transceiver(char cData)
{
/* Start transmission */
SPDR = cData;
/* Wait for transmission complete */
while(!(SPSR & (1<<SPIF)));
/* Return newly received data */
Return SPDR;
}

## Slide 107: SPI - Duplex Mode
char SPI_Tranceiver(char cData)
{
/* Start transmission */
SPDR = cData;
/* Wait for transmission complete */
while(!(SPSR & (1<<SPIF)));
return SPDR
}

## Slide 108: Working with Multiple Slave
All the Slaves share the same MOSI, MISO and SCK signals.
The SS’ signal is responsible for choosing a particular Slave.
The Slave gets enabled only when its input SS’ signal goes LOW.

## Slide 109: SPDR buffer
The system is single buffered in the transmit direction and double buffered in the receive direction.
This means that bytes to be transmitted cannot be written to the SPI Data Register before the entire shift cycle is completed.
When receiving data, however, a received character must be read from the SPI Data Register before the next character has been completely shifted in. Otherwise, the first byte is lost.

## Slide 110: Data Modes
There are four combinations of SCK phase and polarity with respect to serial data, which are determined by control bits CPHA and CPOL.
Data bits are shifted out and latched in on opposite edges of the SCK signal
  ensuring sufficient time for data signals to stabilize.
Sample = Data Reading
Setup = Shifting

## Slide 111: Data Modes

## Slide 112: Data Modes

## Slide 113: Bit Banging (Not for exams)
SPI can also be done without using any dedicated hardware of the uC.
The SPI properties are simulated by programming
The technique is called Bit Banging

## Slide 114: SPI resources
http://maxembedded.com/2013/11/the-spi-of-the-avr/
http://maxembedded.com/2013/11/serial-peripheral-interface-spi-basics/
http://www.avrfreaks.net/forum/atmega32-spi-sample-code
http://www.circuitstoday.com/how-to-work-with-spi-in-avr-micro-controllers
http://www.embedds.com/serial-peripheral-interface-in-avr-microcontrollers/

## Slide 115: Bit Banging
https://electronics.stackexchange.com/questions/44670/what-is-bit-banging
https://en.wikipedia.org/wiki/Bit_banging

## Slide 116
☺