## Slide 1: TIMER in atmega32
Md. Tareq Mahmood

## Slide 2: One more Slide???

## Slide 3: Learning Objective
What is timer?
When, how to use timer?

## Slide 4: Time is “money”
An embedded system has to preform various time-related tasks
  Recording the time when an event occurs
  Calculating the time difference between two events
  Performing tasks at specific or periodic time instants
  Creating accurate time delays
  Generating waveforms of certain shape, period or duty cycle

## Slide 5: Software technique?
Can we use CPU to do these tasks?
  Yes!
  But…
    CPU will be busy
    Timing will not be accurate
Need something special?
    Hardware technique

## Slide 6: PROBLEM DELAY_MS
If an ISR is fired during the execution of a delay_ms(),
ISR will be serviced first, then delay will continue
Resulting in more delay than specified
For example,
If you call _delay_ms(1) and some ISR occurs that take 200us to be serviced, _delay_ms(1) takes 1.2ms

## Slide 7: Overview
ATmega32 has 3 timers
  Timer 0, 1, 2
  Timer 1 has the most functionalities
Each timer is associated with
  A counter
  A clock signal
    Internal
    External

## Slide 8: Overview
When the internal system clock is used, a prescaler can be used to make the timer count at a slower rate
Example:
  Suppose the system clock rate = 1Mhz (1μs per cycle).
  Suppose a timer prescaler of 64 is used.
  Then, timer will increment every 64μs.

## Slide 10: PWM
Pulse Width Modulation
A technique for getting analog results with digital means.
An example of PWM in an idealized inductor driven by a ■ voltage source modulated as a series of pulses, resulting in a ■ sine-like current in the inductor.

## Slide 11: Timer 1

## Slide 12: Timer 1
16 bit counter
  prescaler: 8, 64, 256, 1024
Can trigger a timer overflow interrupt
  and other things.. We will learn those in the subsequent lectures
Can trigger an input capture interrupt when an event occurs on the input capture pin
  timer value is stored automatically in a register.
  input capture pin for Timer 1 is ICP1 (D.6)

## Slide 13: Timer 1 – Relevant pins

## Slide 14: Related Registers – Timer1
TIMER/COUNTER1
  TCNT1
  16 bit register that stores the current value of the counter
Timer/Counter 1 Control Registers
  TCCR1A and TCCR1B
  To configure the operations of Timer 1.
Interrupt registers
  TIMSK to enable timer interrupts
  TIFR to monitor status of timer interrupts

## Slide 15: Related Registers – Timer1
4. Input Capture Register
- ICR1
- to store timer value when an event occurs on input capture pin
5. Output Compare Registers

## Slide 16: Timer related interrupts

## Slide 17: Today’s mission
Creating an accurate delay using timer overflow interrupt
Measuring elapsed time between two events

## Slide 18: Let’s start!!!

## Slide 19: MODES

## Slide 20: Timer/Counter 1 Control Register A (TCCR1A)

## Slide 21: Timer/Counter 1 Control Register B (TCCR1B)

## Slide 22: Clock select

## Slide 23: Normal mode

## Slide 24: Timer/Counter Interrupt Mask Register (TIMSK)

## Slide 25: Timer/Counter Interrupt Flag Register (TIFR)

## Slide 26: Write a C code to toggle PORTB every 2 seconds using TIMER 1 Overflow Interrupt

## Slide 27: Creating an accurate delay of 2s
System Default Frequency: 1Mhz
Period: 1µs
With no prescaler TIMER 1 will increment every 1µs
TCNT1 is 16 bit
Timer will overflow every 216 μs.
How many times TIMER1 will overflow ??
In 2S, total TIMER1 overflow

## Slide 28: C Code
#include <avr/io.h>
#include <avr/interrupt.h>
volatile int overflowCount;
ISR(TIMER1_OVF_vect)
{
  overflowCount++;
  if(overflowCount==31)
  {
  PORTB = ~PORTB;
  overflowCount = 0;
  }
}
int main(void)
{
  overflowCount = 0;
  DDRB = 0xFF;
  PORTB = 0xFF;
  //configure timer
  TCCR1A = 0b00000000; // normal mode
  TCCR1B = 0b00000001; // no prescaler, internal clock
  TIMSK = 0b00000100; //Enable Overflow Interrupt
  sei(); //Global Interrupt Enable
  while(1);
}

## Slide 29: Appendix
Why volatile variable?
  http://www.avrfreaks.net/forum/whats-volatile-variable

## Slide 30: Measure the time for a demo C Code to execute

## Slide 31: Measuring elapsed time

## Slide 34: Thanks everyone!